## Slide 1: Sensors Expo Demos Kanpai + Hidden Light Monitoring Demos
24 July 2017
US-CMS Applications Engineering

## Slide 2: Summary
Kanpai Sensor : Demo to show how the BH1747 color sensor can identify “colors” of the object that is placed on the platform/coaster. Includes additional white LED with color sensor pairing.
Hidden Light Monitoring Sensor : Demo to show how the BH1747 works under 1% lighting conditions. Shows operation as ALS and as a color filter. Only BH1747 behind a 1% transparent glass
Hidden Light Monitoring
Kanpai Sensor Demo

## Slide 3: Kanpai Sensor Demo Setup
HW Used:
  Arduino Uno
  Xbee Shield
  Xbee USB Dongle
  Xbee Transceiver… x2
  Breakout Board for LED+BH1747
Explanation:
  I have setup the Xbee units to only send serial messages to each other. The USB dongle can be connected to a PC to open a COM port. Then will immediately start streaming data
  Color Sensor is connected as follows:
    BH1747 Vdd -> Arduino 3.3V
    BH1747 GND -> Arduino GND
    BH1747 SDA -> Arduino SDA
    BH1747 SCL -> Arduino SDL
  LED is also connected to the 5V source on the Arduino. A standard resistor divider is used to limit current to 5mA.

## Slide 4: Hidden Light Monitoring Sensor Demo Setup
HW Used:
  Arduino Uno
  Xbee Shield
  Xbee USB Dongle
  Xbee Transceiver… x2
  Breakout Board for BH1747 only
Explanation:
  I have setup the Xbee units to only send serial messages to each other. The USB dongle can be connected to a PC to open a COM port. Then will immediately start streaming data
  Color Sensor is connected as follows:
    BH1747 Vdd -> Arduino 3.3V
    BH1747 GND -> Arduino GND
    BH1747 SDA -> Arduino SDA
    BH1747 SCL -> Arduino SDL
  There is no LED used in this demo, so you will need to use an external light source to properly show the operation of this demo
  I also added the “clear” ALS return value to help show the ambient light portion of the demo.

## Slide 5: Resources
GitHub Repository (Firmware)
  https://github.com/ROHMUSDC/SensorExpo2017-Demo-KanpaiandHiddenLight
Xbee Helpful links
  https://www.digi.com/products/xbee-rf-solutions/2-4-ghz-modules/xbee-zigbee
  https://www.digi.com/products/xbee-rf-solutions/xctu-software/xctu
Arduino
  https://store.arduino.cc/usa/arduino-uno-rev3
  https://www.arduino.cc/en/Guide/HomePage
Tera Term
  https://ttssh2.osdn.jp/index.html.en